## Slide 1: Wigram Basin Upgrade
Retrofitting an Existing Blue-Green Asset

## Slide 2
WIGRAM BASIN

## Slide 3: Today’s presentation
History
Changes & drivers
Challenges
Interesting bits
Conclusions

## Slide 4
1990s

## Slide 6: Stormwater in Christchurch
Drainage
Surface Water Management
New Christchurch City Council
New multi-disciplinary approach

## Slide 7: Stormwater in Christchurch
Drainage
Surface Water Management
New Christchurch City Council
New multi-disciplinary approach
Ecology
Recreation
Landscape
Culture
Drainage
Heritage
SIX
VALUES

## Slide 8: Original Wigram Basin design
Flood retention basin, plus water quality treatment
Landscape plantings
  Emergent and amphibious
  Shrubland and woodland
  Habitat and a link to river
Anticipated future development
Notes: A 2.6 ha online wet pond with 22,000 m³ of permanent water volume
A control structure at the wet pond outlet, with a 750 mm diameter outlet pipe to the Ōpāwaho/Heathcote River
An adjacent dry basin, which the wet pond spills to in larger events, providing an additional 135,000 m³ storage (up to embankment level) for up to the 2% AEP event
An embankment around the dry basin, with 20 m spillway to the Ōpāwaho/Heathcote River for over-design events.
Landscape plantings
  Emergent plants and amphibious sward to trap sediment and improve nutrient removal
  Swamp shrubland and kanuka woodland to provide buffer
  Habitat for wildlife and a link to the Ōpāwaho/Heathcote River riparian plantings.
Anticipated development in the catchment leading to increased runoff and contaminant loads
concept design for adding further treatment (a sediment forebay and a primary wet pond) upstream of the basin, converting the basin to a secondary wet pond.

## Slide 10: Change over time
1993
Original Wigram Basin construction
2017
Wigram Basin upgrade
2010/11
CSM1 construction
2010/11
Canterbury Earthquake Series
1998
Sediment forebay & overflow swales
2010
Embankment raised
2012
Low flow outlet & swale
Catchment development
Canterbury Agricultural Park development
Basin habitat growth

## Slide 11: 2010/11 Earthquakes
Increased flood risk in Ōpāwaho/Heathcote River
  Loss of channel capacity
  Tectonic uplift (loss of grade)
  Land settlement
Ōpāwaho/Heathcote River Floodplain Management Programme
  Storage – upper river
  Dredging – lower river
  Low stopbanks feasibility
  Flood Intervention Policy
Loss of QEII sports facility
New Ngā Puna Wai sports hub

## Slide 12: Drivers for Wigram Basin upgrade
Storage in upper Ōpāwaho/Heathcote River
Water quality treatment
Ngā Puna Wai sports hub

## Slide 13: Brief
Additional flood storage
Wetland treatment
Limited footprint (wet area and dry basin)
Minimise the peak discharge
Minimise the frequency of ponding on the dry basin

## Slide 14: Brief

## Slide 15
WET
EQUESTRIAN
POLO
NGĀ PUNA WAI SPORTS HUB
A & P SOCIETY

## Slide 17: Challenges
Can’t achieve full first flush/water quality treatment
Need to achieve a balance between:
  Treatment
  Water levels in wet pond
  Attenuation of outflows
  Flooding of dry basin
Need to understand performance in day-to-day flows & small events

## Slide 18: Modelling
Existing event based models by others – large events (10 to 200 yr)
New continuous simulation model – small and sequential events
Concept
Test
Refine

## Slide 19: Concept design
Modify the existing wet pond – settlement and buffer storage
Create a new wetland – treatment
Back-flooding over the wetland – additional storage & treatment
Modify the existing dry basin – flood storage
Notes: Modify the existing wet pond – to work as a first flush basin providing settlement and buffer storage to control the flow rate into the wetland.
Create a new wetland – to provide wetland treatment of the outflow from wet pond under normal flow conditions and small storm events, prior to discharge to the river.
Back-flooding over the wetland – to provide additional storage and some treatment, in larger events.
Modify the existing dry basin – lowering ground levels over the dry basin to provide additional storage in major storm events.

## Slide 20: Modelling
Hydrology
HEC-HMS
Rainfall: 62 years
Runoff: Baseflow, pervious & impervious
Calibration: 21 years of basin water level data  synthetic flow record

## Slide 21: Modelling
Annual volume
Chart: Annual volume (million m3)
| 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016
Wigram Basin outflow | 2406399.049 | 2282074.3511 | 1904575.3428 | 2151020.5212 | 1963094.164 | 1979842.1674 | 3159155.5062 | 2405058.1125 | 3036947.9397 | 2724783.2922 | 3450566.5946 | 2720408.9353 | 3378914.5078 | 2537026.4138 | 2754195.6171 | 2364360.084 | 2727709.9994 | 4054994.1755 | 3208682.6717 | 924447.3725 | 1242995.5996
Modelled flow | 2798046.36 | 2492131.68 | 2506247.73 | 2587391.37 | 1989617.04 | 2205362.52 | 2833323.66 | 2185643.79 | 2676092.49 | 2350169.46 | 2947978.44 | 2377237.59 | 2661416.82 | 2401352.37 | 2464060.23 | 2765716.92 | 2724861.24 | 2797123.95 | 2880404.37 | 1033233.084 | 1212281.532

## Slide 22: Modelling
Frequency curves

## Slide 23: Modelling
Hydraulics
InfoWorks ICM
Concept: storage nodes, pipes & hydraulic controls (nodes & weirs)

## Slide 24: Modelling
Hydraulics
InfoWorks ICM
Concept: storage nodes, pipes & hydraulic controls (nodes & weirs)
Options - changing:
  Discharge
  Residence time in wetlands
  Bund heights
  Buffer storage operation

## Slide 25: Modelling
Results
Frequency & duration of elevated water levels & ponding
Percentage of inflow through wetland - low flow & spillways

## Slide 26: Modelling

## Slide 27: Final design

## Slide 29: Numbers
220,000m³ additional live storage
3.6ha wetland
92% inflow volume goes through wet pond and wetland low flow
3% via overflow weirs from the wet pond to the wetlands
5% directly from the wet pond to the Ōpāwaho/Heathcote River
Average wetland retention time is 4.2 days

## Slide 30
ECOLOGY
CONSENTS
LANDSCAPE
COST
GEOTECH
Civil
STORMWATER DESIGN
Construction & operations
STRUCTURAL

## Slide 31
ECOLOGY
CONSENTS
LANDSCAPE
COST
GEOTECH
Civil
STORMWATER DESIGN
Construction & operations
STRUCTURAL

## Slide 32: Landscape & ecology
Removal of exotic trees
Minimising disturbance to existing vegetation & birds
New native plantings:
  Wetland (shallow, deep, bench, embankment)
  Floodplain
  Dryland
Pedestrian, cycle and horse paths
Fish passage
Notes: Pedestrian, cycle and horse paths – levels and separation
Fish passage – short fin eels

## Slide 33: Adaptability for future change
Adaptability
  Modelling not perfect
  Inflow will change over time with changes in climate and catchment
Adaptable hydraulic controls
  Orifices and weirs in structures (rather than pipes) used to limit flow
  Orifices in replaceable slide gates (rather than in concrete structure)
  Weirs in structures are stopboards or slide gates (rather than concrete)
  Penstocks (rather than slide gates) in key locations – can be actuated

## Slide 35
NGĀ PUNA WAI SPORTS HUB
WIGRAM BASIN
Ōpāwaho /
HEATHCOTE RIVER

## Slide 36: Conclusions
Original basin – new innovative ‘six values’ approach
Changes in upstream catchment & downstream river meant that upgrade was required
Innovative approach required to achieve treatment & storage in tight footprint
Continuous modelling key tool in design
Final design developed by multi-disciplinary team – continues ‘six values’ approach