## Slide 1: Bridge Manual Waterway Design: An Update
Iain Smith – Beca
Nigel Lloyd - NZTA

## Slide 2: Introduction
Background
Proposed amendments
Residual issues
What is next?

## Slide 3: Background

## Slide 5
v

## Slide 6: Proposed Amendments

## Slide 7: Council Requirements
River “design” corridor
River management practices
Council standards – flood impact
Ecology - no piers in the river
Scour protection

## Slide 8: Models
Hydrological
Hydraulic
One source of the “truth”
Complex systems need to be modelled

## Slide 12: Backwater Control
Lakes, rivers, the sea
Which dominates what
Event combinations
Risk approach

## Slide 13: Climate Change
2018 MfE guidance?
Rainfall - HIRDS V4
Flood frequency hydrology: +20 to 25% peak flow
Sea level rise: MfE 2017

## Slide 14: Hydrology
Other Methods: SCS
MPD
Sensitivity checking
HIRDS as a preference
Rational method changes

## Slide 15: Flood Impact (Afflux)
“No impact” = unrealistic
What is acceptable then?
Don’t forget drain down

## Slide 16: Proposed Amendments

## Slide 18: Major Culvert Criteria
Limited to 2m heading up
Fish passage
Debris – AR&R risk approach
Bed transport processes

## Slide 19: Cohesive Bed Scour
Difficult issue
Estimated by non-cohesive scour
Reference Austroads Part 8 & HEC 18

## Slide 20: Residual Issues

## Slide 21: Complexity

## Slide 22: Climate Change
Rainfall
  MfE 2008 - 2.1o to 2090
  MfE 2018 - RCP ??? to 2081 – 2100?
  RCP 6 for design and 8.5 as a sensitivity?

## Slide 23: SLS and ULS
Serviceability Limit State:
  “undamaged” in a SLS 1 (1 in 25yr) flood
  “not significantly damaged” (1 in 100yr) in an SLS 2 flood
  Too nuanced. Remove distinction.
Ultimate Limit State: protection for an overflow in a 1 in 2,500 yr ARI flood? Confirm expectations or remove.

## Slide 24: Coastal Structures
Expert coastal advice needed
Document in Structure Options Report / Design Statement

## Slide 25: Major Culvert Freeboard
Is it a bridge or a culvert?
Cross sectional area larger than 6m2
300mm from SLS 2 flood level to soffit

## Slide 26: Waterway Diversions
Geomorphology, bank stability, habitat features, riparian planting
Bridge Manual doesn’t cover this

## Slide 27: Rock Rip Rap
Rock quality
Size and mass grading envelope
Standard Technical Specification needed

## Slide 28: Where next?

## Slide 29: Questions