## Slide 1: Temporal Rainfall: A Risk Based Approach
Water New Zealand’s 2019 Stormwater Conference
Andrew Boldero Work Group Manager - Water Resources WSP Opus Hamilton, New Zealand
Zaki Matar Water Resources Engineer WSP Melbourne , Australia

## Slide 2: Agenda
Australian Rainfall and Runoff Prediction methodology
New Zealand Rainfall and Runoff Prediction methodologies
New Zealand’s HIRDS (version 4 update)
Test case and results
Comparison of methodologies (Australia and New Zealand)
Discussion/Next stage/Collaboration
Questions

## Slide 3: Australia
Australian Runoff and Rainfall (ARR) is a National standard for Hydrologic and Hydraulic Modelling
ARR recently released a new edition (ARR 2016), with substantial changes to design flood estimation when compared to from the previous version ARR1987
Uptake of ARR2016 has been gradual due as existing software is updated to align with the new guidelines

## Slide 4: Australia: From ARR1987 to ARR2016
Notes: Briefly go through Key changes: particularly IFD, losses and temporal patterns
The Australian Bureau of Meteorology undertook an extensive review of Intensity-Frequency-Duration rainfall data across Australia. As part of this work, a pluviograph database containing a total of 2280 stations across Australia was produced
Pre-burst rainfall is now an important consideration in Australian design flood estimation

## Slide 5: Australia: Temporal pattern time development time line
30 years of additional climate data is available since the 1987 edition of ARR
An Australia-wide study of temporal patterns is undertaken using climate records to derive regional ensemble patterns to use in design applications.
Variability of actual patterns is much less important than central tendency (AVM)
It is established by various studies between 1975 and 1994 that temporal patterns exhibit significant variability between rainfall events of similar magnitude
To overcome simplification, there is an increasing preference to adopt a probabilistic and regional based approach to temporal pattern selection
Ensemble method with selection of a representative temporal pattern is recommended in design flood estimation
The adopted pattern can have a significant effect on the estimated peak flow. The effect is greatest in catchments with large storages.
ARR1987
ARR2016
Notes: Flood estimation in urban catchments moves toward storage-based mitigation solutions

## Slide 6
Australia: Urban flood modelling flow chart
  An ensemble of 10 temporal patterns were generated by the study
    per AEP (Rare Intermediate and Frequent)
    per duration (5 minutes to 7 days); and
    per temporal pattern region.
12 Climate regions across Australia were defined in ARR2016 as part of detailed study
Delineation of temporal pattern regions was based on drainage basin boundaries and ‘burst loading’
Notes: Design temporal runoff patterns across Australia were generated as part of a detailed study involving 35 test catchments
Temporal rainfall patterns vary regionally across Australia and twelve temporal pattern regions have been defined (Figure 4). The regions follow key drainage basin boundaries and vary with ‘burst loading’. ‘Burst loading’ is essentially a simple measure of when the heaviest part of the burst occurs, with categories labelled accordingly as front, middle and back loaded events
Each ensemble contained carefully selected temporal patterns, based on consideration of several temporal pattern selection criteria.

## Slide 7: ARR online data hub
Temporal Patterns are available for the AEP classes shown in the below graphic
The ensemble temporal patterns are available publicly and can be accessed through the ARR online data hub.
The data hub simply requires spatial co-ordinates of the study area to produce several characteristics of the study area, including temporal patterns

## Slide 8: Selection of a represent-ative temporal pattern
Key considerations for the selection process
The criteria/metrics that are being adopted (Eg. Flood levels? Pipe flows?)
  For urban environments peak flood levels are usually a better indicator of flooding behaviour than the overland or drainage flow.
  What happens when more than one metric is important? Short answer: Consider all of them
Eg. Pipe flows

## Slide 9: New Zealand
Common New Zealand Runoff Estimation Methodologies:
Technical Publication (TP) 108: Guidelines for stormwater runoff modelling in the Auckland Region (April 1999)
Rational Method (Kuichling (1889) – peak flow only
Hydrological and hydraulic simulation modelling

## Slide 10: New Zealand
Hydrological Simulation Modelling – Temporal rainfall patterns:
  Empirical data (Actual rainfall data)
  TP108 (1999)
  High Intensity Rainfall Design System (HIRDS) recently updated (2018)
  Probable Maximum Precipitation (PMP) developed early 1990s

## Slide 11: New Zealand
HIRDS version 4 (NIWA 2018)
Uses empirical rainfall data up to and including 2015
6 climate regions across NZ
Utilises a non-dimensional asymmetric hyberbolic tangent function

## Slide 12: New Zealand
HIRDS version 4 (2018)
Example (6 hour duration) graph
Front and rear loading is removed
Steep intensities are averaged/reduced
Multi-peaked events are distributed across a singular peak/not represented

## Slide 13: New Zealand
TEST CASE
A New Zealand Sample site with calibrated model (downstream measured flow data) was selected with a catchment size of 18km2
Selection of various temporal rainfall patterns across Australia (Hobart, Melbourne and Sydney) were applied to the test site.
An additional run was also completed for the Melbourne data where the temporal rainfall pattern was averaged to see what effect this could have on the results.

## Slide 14: New Zealand
Temporal Pattern Comparison from Melbourne (1% AEP)
The two most extreme temporal patterns were selected from each location (orange and black). The averaged pattern is show in blue.

## Slide 15: New Zealand
TEST RESULTS
Runoff flow result comparison:
Raw temporal rainfall patterns all showed peak flow increases ranging from +16% to +83%
Sydney patterns provided a peak flow variance of 45%
Hobart patterns provide a peak flow variance of 11%
Melbourne patterns provided a peak flow variance of 43%
As expected, unitless rainfall patterns showed minimal variance in total runoff volumes
When compared to an averaged Melbourne temporal pattern the peak flows were similar to the measured results (-3%).
Recorded Flow |  | Recorded Rainfall | PMP | TP108 | Sydney Temporal Pattern |  | Hobart Temporal Pattern |  | Melbourne Temporal Pattern |  | 
 |  |  |  |  | 6882 | 6857 | 4719 | 4723 | 5826 | 6032 | Average Melbourne Temporal Pattern
Peak (m³/s) | 46.85 | 44.1 | 50 | 59.4 | 75.3 | 54.5 | 71.3 | 76.5 | 85.6 | 65.4 | 45.6
Volume (Mm³) | 1.52* | 1.07 | 1.07 | 1.93 | 1.07 | 1.07 | 1.07 | 1.07 | 1.07 | 1.07 | 1.07
Peak flow % variance | Base | 6% | 7% | 27% | 61% | 16% | 52% | 63% | 83% | 40% | -3%

## Slide 16: Summary
NEW ZEALAND
1 ‘smoothed’ temporal rainfall pattern used
District/Council standards
6 Climate regions (HIRDSv4)
2 Climate regions (PMP)*
Relatively small climate regions
Rainfall data updated
HIRDS Version 4 updated 2018 (using 2015 data)
No methodology update
AUSTRALIA
10 ‘raw’ temporal rainfall patterns used
National standard (ARR)
12 Climate regions
(including tropical zones)
Large climate regions
Rainfall data updated
ARR 2016
Methodology updated 2016 as part of ARR review
* plus alpine regions

## Slide 17: What is Next?
To answer the question ‘is a risk based approach suitable for New Zealand?’
More data is needed to enable a detailed analyse of the alternative methodology in the New Zealand Climate
Next Steps:
Industry Collaboration
Undertake simplified ARR2016 methodology utilising NIWA’s raw temporal data.
Collate and analyse results
Share results with Industry
Contact:
andrew.boldero@wsp.com

## Slide 18: Questions
Contact:
andrew.boldero@wsp.com