## Slide 1: Water Pipe Burst Analysis
October 2022
Water New Zealand Conference

## Slide 2: Introduction
Collaboration
Computation
Comparison
Checking
Correction

## Slide 3: The WDC Pipe Burst Model
Water Pipe Bursts are a record of a pipe’s performance
Used as a surrogate for determining the condition of pressure pipe
Based on the principal that as a pipe ages the risk and frequency of bursts increase over time
The key purpose of the work is to estimate the expected life of a pipe to inform long term renewals

## Slide 4: Source Data
Forms filled out manually by the Council Water Unit
Collected as paper forms until approximately 2018
Most collected electronically since

## Slide 5: Cleaning up the Data
Water Unit Forms put into an Excel database
Matched to a pipe using address information and assigned a GIS point
Records going back to 2007 (paper records go back further)
Last updated up to end of 2019
Current AMIS system collects all new data electronically from the field

## Slide 6: Pipe Groups
Pipe Burst Analysis done using Pipe Groups
Pipe Grouping used to reflect the fact that similar pipes should perform in the same fashion
Attributes such as size, material, age of install and location used to determine pipe groups

## Slide 7: Analysis: Repairs by Age of Pipe
First considered repairs per km by age of pipe to determine a relationship
Showed clear relationship between age of pipe and number of repairs
Didn’t fully take into account the length of pipes at different ages and the age at which the repairs took place

## Slide 8: Analysis: Cumulative Repairs by Age
Determining the total number of repairs as the pipe ages
Advantage with this approach is that it takes into account the relative network lengths over which repairs can occur
Bursts occurring in older pipes generally occur over a smaller sample size therefore the effect is greater

## Slide 9: Analysis: Pipe Groups
Using Pivot Table able to assess different pipe groups to determine whether unique relationships exist
Needed to adjust graphs to account for missing repair data (pre 2007)
Blue line shows raw data profile
Red line shows adjusted profile
Exponential Relationship determined

## Slide 10: Results
Table showing total bursts per km by age for each pipe group
Can be used to define a Level of Service for each pipe group (ie the point at which the pipe is considered to be at the end of its useful life)
Further economic analysis can be used to help inform which Level of Service is appropriate

## Slide 11: Comparison with Historic Records
Analysis with historic annual records showed significant annual variation in burst rates but good long term alignment with model outputs

## Slide 12: Long Term Forecasting
Burst model combined with Renewals Model to assess future burst rates based on current renewals expenditure
Can be used to assess future condition of network and forecast frequency and cost of mains repairs
Can forecast number of connections affected and expected impact on consumers

## Slide 13: Comparison between WDC and SDC Data
Good correlation between the two datasets for some pipe groups
SDC data showed small diameter AC pipes to be performing better in Selwyn DC conditions
SDC data showed small diameter Modern PE pipes to be performing poorly when compared with larger diameter modern pipes

## Slide 14: What is the cause of the greater number of small modern PE failures?

## Slide 15: Other uses of the data
Checking ‘useful life assumptions’
Level of service discussions
Renewal strategy
Data correction

## Slide 16: Closing comments
Collaboration
Computation
Comparison
Checking
Correction

## Slide 17: Questions?