## Slide 1: Permeable reactive barriers for the removal of nitrate in shallow groundwater
Weaver, L.,1 Burbery, L., 1* Webber, J.,1 Dupont, P-Y.,1 Taylor, W., 1 Abraham, P.,1 McGill, E.,1 Sitthirit, P.,1Close, M. 1
1 Institute for Environmental Science & Research Ltd. (ESR)
* Currently at Dairy NZ
Notes: Tena koutou
No Wolverhampton ingarani ahau.
I tipu ake au i Portsmouth, Ingarangi.
No Ingarani oku tipuna.
No kororo kororo, Otautahi ahau.
Ko Louise Weaver toku ingua.

## Slide 2: Content
The nitrogen cycle – balanced and unbalanced
Denitrification – the PRB
Site description & methods
Results
Conclusions
Notes: Today we will focus on groundwater. One of the major contaminants of concern is nitrate. Coupled to a wider programme investigating the use of reactive barriers to remove nitrate we investigated the impact of such system on biology and function in shallow groundwater.

## Slide 3: Nitrogen cycle
Notes: Nitrogen cycle vital for life on Earth. Atmospheric N2 is converted to a form that plants can incorporate into new proteins.
Fixation – nitrogen-fixing bacteria convert N2 to NH3. Anaerobic process. Often occurring in rhizomes.
Nitrification – soil bacteria convert ammonia into nitrate. Can be used by plants and animals. Two step process by two groups of bacteria. Chemotrophs.
Assimilation – plants consume nitrates to make building blocks of life.
Ammonification – converts breakdown of amino acids and nucleic acids into nitrates and ammonia.
Final step – DENITRIFICATION. Anaerobic bacteria convert nitrates to N2 gas.
The nitrogen cycle is a process that can occur through microbially driven processes and autotrophic processes. For denitrification to occur suboxic conditions are normally required. Herein lies the problem for many of our shallow aquifers.

## Slide 4: Nitrate and denitrification
Denitrification (DeN) - natural process carried out by facultative bacteria
DeN organisms respire nitrate in lieu of oxygen
Require food (energy) source e.g. organic carbon
Harmful nitrate converted to innocuous N2 gas
N2 gas
carbon
food
nitrate
Bacteria
O2
O2
O2
Food
DeN
Bacteria
Notes: Denitrification is a microbially facilitated process where nitrate is reduced and ultimately produces molecular nitrogen (N2) through a series of intermediate gaseous nitrogen oxide products.
Anaerobic bacteria perform denitrification as a type of respiration that reduces oxidized forms of nitrogen in response to the oxidation of an electron donor such as organic matter.

## Slide 5: Denitrification wall Permeable reactive barrier
Enhances removal of nitrate in shallow groundwater systems
Solid organic matter (e.g. woodchips) is placed in trenches intercepting nitrate contaminated groundwater
Organic matter is a substrate and carbon source for microbes
Nitrate reduced to nitrogen gas
Notes: Denitrification walls (which is a PRB for nitrate removal) enhance the removal of nitrate in shallow groundwater systems.
The barrier is a trench filled with solid organic matter (for example woodchips) that passively intercepts the nitrate contaminated groundwater.
The organic matter is a substrate for growth and a carbon source for a microbial community.
As nitrate rich groundwater flows into the barrier, the organic matter stimulates microbial activity, removing nitrate from the groundwater as inert nitrogen gas.

## Slide 6
Cambridge, Waikato
Photo: Louis Schipper
Sand w/ silt & clay
Kaquifer ~65 m/d
velocity <0.5 m/d
30/70 sawdust/spoil
Schipper et al., 2004
First trials 1990’s:
  Robertson & Cherry (1995):
  Long Point, Ontario, Canada
  Schipper & Vojvodic-Vukovic (1998):
  Hautapu, Cambridge, NZ
Prognosis 30 years operational life
Notes: Many examples now globally.
Louis Schipper – Waikato.

## Slide 7: What about shallow gravel aquifers?
sand
open framework gravel
sandy gravel
sandy gravel
sandy gravel
gravel
gravel
gravel
Heterogeneous
Highly permeable OFG
  Kgravel ~104 m/day
  Ksand ~102 m/day
Notes: OFG is complex – not homogenous. Extreme fast open channels.

## Slide 8
sandy gravel
gravel
Fast-flowing
  velocities 10-100’s m/day
  preferential flow via OFG
High mass fluxes
  water
  dissolved oxygen
  nitrate
Viability assessment:
  1. Technical performance
    hydraulic efficiency & denitrifying capacity
  2. Any adverse effects (pollution-swapping phenomena)?
      DOC export; arsenic release
      GHG emissions
  3. Pragmatism; cost-effectiveness – can we dig below the water table?
Notes: Are PRB viable in OFG?

## Slide 9: Study site: Silverstream, North Canterbury
Old North Branch Waimakariri River
Unconfined gravel aquifer ~5 m thick
Water table within 0.5 m ground level
Groundwater nitrate 6–7 mg/L NO3-N
Report on the Waimakariri, Geo Nelson (1928)
Notes: Are PRB viable in OFG?

## Slide 10: Wall construction November 2018
flow direction
Excavation shored & dewatered = expensive!
3 m deep; partially penetrates aquifer
Initially, Kwall ~ 10 x Kaquifer; induced ~15% more flow
152-230 m3 water/day; 340-588 kg N/year
25 m long
5 m
wide
3 m
deep
Aquifer material >20 mm / “hogged wood”
CELL 2
Porosity 43%
K ~20,000 m/d
20 -40 mm gravel / “chipped wood”
CELL 1
Porosity 50%
K ~30,000 m/d
Specific discharge, q = 2.6 m/d
100 x flow at Long Point, Canada
12 x flow at Hautapu, Waikato
Notes: Are PRB viable in OFG?

## Slide 11
Monitoring:
Groundwater level (daily)
Piezometric survey quarterly
GHG emission - 12 months
Frequency | # wells | Parameters
Weekly-monthly | 9 wells along flowline | pH, temperature, DO, ORP, EC NO3, NO2, NH4, DOC alkalinity, SO4, DRP, Fe, Mn, As
Quarterly | +13 wells distributed across site | pH, temperature, DO, ORP, EC NO3, NO2, NH4, DOC dissolved CH4 & N2O
6 months | 7 wells transecting woodchip wall | pH, temperature, DO, ORP, EC NO3, NO2, NH4 alkalinity, SO4, DOC, DRP, Fe, Mn, As major ions DNA in water & biofilm extract stygofauna
Notes: Are PRB viable in OFG?

## Slide 12
Notes: Evident a nitrate-free plume of groundwater traceable downstream from wall. Mixes/dilutes with regional flow field, as migrates NE.

## Slide 13: Wells installed
Perspex wells – PX
PVC wells – S
Well | Diam (mm) | Screen (m bgl) | Location | Biobag type & position
PX1 | 100 | 1.5 – 2.5 m | Upstream | Round gravel biobag. Sampler top 1.5 m.
PX2 | 100 | 1.5 – 2.5 m | Start of PRB | Round gravel biobag. Sampler top 1.5 m deep.
PX3 | 100 | 1.5 – 2.5 m | Mid PRB | Round gravel biobag AND Woodchip biobag. Sampler top 1.5 m deep.
PX4 | 100 | 3 – 4 m | Beneath PRB | Wide sampler, 2x round gravel biobag. Sampler top 3 m deep.
PX5 | 100 | 1.5 – 2.5 m | Downstream | Wide sampler, 2x round gravel biobag. Sampler top 1.5 m deep.
S7 | 50 | 1 m up/lower | Downstream | Oblong gravel biobag. Sampler top 1.5 m deep.
S8 | 50 | 1 m up/lower | Downstream | Oblong gravel biobag. Sampler top 1.5 m deep.

## Slide 14
PX1
PX2
PX3
PX4
PX5
S7
S8
Groundwater flow direction
-10 m
wall
+10 m

## Slide 15: Methods
Sampling
Groundwater
Biobags - biofilms
Sequencing
Archaea & bacteria
Eukaryotes
Analysis
Abundance
Changes across transect over time
Fungi
DNA
DNA

## Slide 16: Results

## Slide 17
-10 m
wall
+10 m

## Slide 18: nitrate
-10 m
wall
C6
C5
C4
+10 m
Groundwater flow direction

## Slide 19: nitrate
-10 m
wall
C6
C5
C4
+10 m
Groundwater flow direction
First 9 months >98% nitrate removal
N = -7.5 mg/L

## Slide 20: nitrate
-10 m
wall
C6
C5
C4
+10 m
Groundwater flow direction
First 9 months >98% nitrate removal
N = -7.5 mg/L

## Slide 21: nitrate
C6
C5
C4
-10 m
wall
+10 m
Groundwater flow direction
Months 9 – 20, ~89% nitrate removal
N = -6.7 mg/L

## Slide 22: nitrate
-10 m
wall
C6
C5
C4
+10 m
Groundwater flow direction
After 20 months, sharp drop to ~55% nitrate removal
Triggered by salt tracer test
N = -3.9 mg/L

## Slide 23: nitrate, nitrite
-10 m
wall
C6
C5
C4
+10 m
Groundwater flow direction

## Slide 24: nitrate, nitrite, ammonium
-10 m
wall
C6
C5
C4
+10 m
Groundwater flow direction

## Slide 25: nitrate, nitrite, ammonium
-10 m
wall
C6
C5
C4
+10 m
Groundwater flow direction
Small initial ammonium export from woodchip (NH4+ <0.2 mg N/L)
Nitrite increase after ~35 weeks; stabilised ~0.14 mg N/L
No evidence of nitrite accumulation in aquifer

## Slide 26
Groundwater flow direction
-10 m
wall
C6
C5
C4
+10 m
Labile carbon leached out from wood within first 6 months
After approx. 18 months, all DOC readings below background
dissolved organic carbon

## Slide 27
C6
C5
C4
Groundwater flow direction
-10 m
wall
+10 m
dissolved reactive phosphorus
Similar pattern to DOC - export from wood within first 6 months

## Slide 28
Groundwater flow direction
-10 m
wall
C6
C5
C4
+10 m
arsenic

## Slide 29
Groundwater flow direction
-10 m
wall
C6
C5
C4
+10 m
arsenic
MAV
10 ug/L
Arsenic mobilised from greywacke aquifer sediments
Acute, localised impact coincident with high DOC/low redox state
Extent of measurable effect 40-70 m down-gradient of wall

## Slide 30: Greenhouse gas emissions
Groundwater flow direction
-10 m
wall
+10 m
Denitrification wall emits less N2O than pasture
Positive CH4 flux – not significant
C6
C5
C4

## Slide 31
S8
S7
PX1
PX2
PX3
PX4
PX5
Notes: Overall groundwater study confirms a decrease in dissolved oxygen within the PRB and a slow recovery downstream. Noticeable shift in communities from aerobic to microaerophilic and anaerobic from PX2 – PX3 & 4, even to PX5 downstream. S7 appears to have another source of influence to it as it consistently showed different results both for 16s and 18s analysis. S8 showed a slow response to the plume but did show ultimately a recovery to increased oxygenic conditions.
Alphaproteobacteria – oligotrophs (capable of living in low nutrient environments.
Gammaproteobacteria – highly diverse, chemolithoautotrophs, heterotrophs etc.
Methanobacteria – methane producers.
Methylomirabilia – anaerobic oxidation of methane. Darker green.
Vicinambacteria – Acidobacteria. Aerobic chemoorganoheterotrophs. Grow on sugars but prefer complex proteinaceous compounds. Incl. chitin degradation.

## Slide 32: Eukaryotic diversity
S8
S7
PX1
PX2
PX3
PX4
PX5
Notes: Dominant phyla – ciliates (ciliophora). Prefer anaerobic/low oxygen conditions. Ciliates are predatory, bacteriovores, omnivores. Here dominance of bacteriovorous spp.
Cercozoa decrease within PRB. Predatory bacteriovores.

## Slide 33: Stygofauna populations
Low abundance upstream
Increase within and downstream of PRB
PX1
PX2
PX3
PX4
PX5
S7
S8
Isopod
Copepod
Copepod
Copepod
Copepod
Amphipod
Amphipod
Notes: Stygofauna still being ID’d. So far we can see increase in activity at the interface in the wall. Exclusive copepods present within, below and immediately downstream of wall. Then reverts to wider diversity present.

## Slide 34: Conclusions & next steps
Nitrate was removed
Biology changed within and downstream
  Driven by change in:
    Oxic conditions
    Food sources
Decrease in diversity of Eukaryotes – dominated by prokaryotic predators
Missed early changes – likely to have missed key changes
What’s next:
How can the barriers be improved?
Are they capable of removing other contaminants present?
PX1
PX2
PX3
PX4
PX5
S7
S8

## Slide 35: Thank you for listening. Any Questions?

## Slide 36
Silverstream Reserve denitrification wall, May 2019
Acknowledgements:
Louise.weaver@esr.cri.nz
Thank you